DIVISION 27 21 29

IFS 8-PORT 10/100BASE-TX + 2- GIGABIT TP/SPF MANAGED SWITCH

GE-DS-82 SERIES

ENGINEERING SPECIFICATIONS

# PART 1 - GENERAL

1.01 SUMMARY

- 8-port Fast Ethernet Managed Switch with 2 Gigabit uplink ports, with additional PoE capability for powering network edge devices

  - SECTION INCLUDES

- 8-port 10/100 BASE-TX + 2-Gigabit TP/SFP managed switch

- 8-port 10/100 BASE-TX + 2-Gigabit TP/SFP managed switch with PoE

1.03 REFERENCES

- Underwriters Laboratory (UL)

- Underwriters Laboratory Canada (ULC)

- European Union Compliance (CE)

1.04 SYSTEM DESCRIPTION

- The IFS Layer 2 Managed Switch shall provide 8 10/100TX ports and 2 Gigabit TP/SFP combination ports delivered in a desktop, compact size case.

- The Gigabit TP / SFP combo ports shall be either 10 / 100 / 1000Mbps on TP ports or 1000Base-SX / LX only through the SFP (Small Form-Factor Pluggable) interface.

- The SFP module shall utilize 850nm optics capable of bi-directional data transmission of 1000Base-SX on two multimode optical fibers.

- The SFP module shall utilize 1310nm optics capable of bi-directional data transmission of 1000Base-LX on two single-mode optical fibers.

- The SFP module shall utilize 1310nm/1490nm or 1310nm/1550nm optics capable of bi-directional data transmission of 1000Base-BX on one single-mode optical fiber.

- The IFS GE-DS-82-PoE Managed PoE Switch shall provide 8 10/100Mbps Fast Ethernet ports and 2 Gigabit TP/SFP combo interfaces with 8 full powered PoE ports.

- The PoE in-line power is compliant with the IEEE 802.3af standard providing 15.4W per port that can power devices at a distance up to 100 meters through the 4-pair Cat 5/5e UTP wire

- Full PoE per IEEE802.3af standards (15.4 W) shall be provided to each of the 8 ports with no PoE sharing between ports.

1.05 SUBMITTALS

- Manufacturer’s Quick Installation Guide and Operating Manual: Printed installation guide and operating information for the Managed Switch.

1.06 DELIVERY, STORAGE AND HANDLING

- Store in original packaging in a climate controlled environment. Storage Temperature not to exceed: -20˚ C to +70˚ C

- Deliver materials in unopened factory packaging with Manufacturer’s bar coding to the job site.

- Inspect product upon delivery to assure that specified products have been received.

1.07 PROJECT/SITE CONDITIONS

- Temperature Requirements:

- The IFS GE-DS-82 or GE-DS-82-PoE shall operate in an environment with an ambient temperature range of 0˚ C to +50˚ C without the assistance of fan-forced cooling.

- Humidity Requirements: Products shall operate in an environment with relative humidity of 20% to 95% (non-condensing).

1.08 WARRANTY

- UTCFS Return and Warranty Policy: UTCFS warrants the product to be free of factory defects for period of 3 years.

# PART 2 - PRODUCTS

2.01 MANUFACTURER

- Acceptable Manufacturer:

- IFS Brand
UTC Fire & Security, Inc.
8985 Town Center Parkway
Bradenton, FL 34202-5129

- Phone 1-855-286-8889

- Email: 	presales@interlogix.com

- Substitutions: Not Permitted

- All fiber optic SFP modules shall be supplied from a single manufacturer.

2.02 MANUFACTURED UNITS

- Model Number Descriptions: Reference Table A: Product Number Descriptions

- Model Compatibility Chart: Reference Table B: Product Compatibility Chart

2.03 GENERAL SPECIFICATIONS

- The Managed Ethernet switch shall be an IFS GE-DS Series model.

- The switch features 8 fixed 10/100TX electrical ports

- The switch features two combination 10/100/1000T electrical ports or 1000SX/LX optical SFP slots.

- The switch shall support the Ethernet data IEEE 802.3 protocol using Auto-negotiating and Auto-MDI/MDI-X features.

- The switch shall provide power, link speed and  PoE In-use status indicating LED’s for monitoring proper system operation.

- The switch shall provide a RS-232 serial connection for local management of the device.

- The switch shall be a 1U (1.75 inches) 13-inch equipment and it can be installed in a standard cabinet or 19-inch rack with included rack mount ears.

- The switch shall be connected with EIA568A/B Cat 5/5e/6 UTP/STP cable system for its RJ-45 interface ports.

- The IFS GE-DS-82-PoE shall comply with IEEE 802.3af Power over Ethernet:

- The IFS GE-DS-82-PoE shall support IEEE802.3af Power over Ethernet detection and 48VDC power injection at port#1 to port#8.

- The IFS GE-DS-82-PoE shall transmit DC Voltage to the Cat5/5e cable and transfer data and power simultaneously to remote PD (Powered Device) equipments.

- The IFS GE-DS-82-PoE shall Auto-detect PoE IEEE 802.3af equipment; protect devices from being damaged by incorrect installation.

- The IFS GE-DS-82-PoE shall support a total distance up to 100 meters on each PoE port.

2.04 DATA SPECIFICATIONS

- Data Interface: Ethernet IEEE802.3/3u/3ab/3z

- Data Rate:

- Port-1 to Port-8: 10/100 Mbps

- Port-9 and Port-10 TP: 10/100/1000 Mbps

- Port-9 and Port-10 SFP: 1000 Mbps

- Data Ports: 10

- Operation Mode: Half-duplex or Full-duplex

2.05 OPTICAL SPECIFICATIONS

- IFS Model Number GE-DS-82 Series

- Optical Interface: 3.3V SFP (Small Form-Factor Pluggable) slot

- Number of SFP Optical ports:2

- Optical Fiber:

- 62.5/125 micron multimode

- 9/125 micron single-mode

- Number of Fibers Required: 1 or 2, vary on SFP module

- Optical Wavelength:

  - 1000SX multimode: 850nm

  - 1000LX single-mode: 1310nm

- Optical Power Budget: vary on SFP module

- Maximum Distance: 74.56 miles (120km)

2.06 STATUS INDICATORS

- System

| 1. | PWR | Green | The switch unit is power on |
| --- | --- | --- | --- |

B. 10/100Base-TX Interfaces

| 1. | LNK/ ACT | Green | Illuminates to indicate the link through that port is successfully established. |
| --- | --- | --- | --- |
|  |  |  | Blink to indicate that the Switch is actively sending or receiving data over that port. |

C. 1000Base-T / SFP Interfaces

| 1. | 1000 LNK/ ACT | Green | Illuminates to indicate the link through that port is successfully established with speed 1000Mbps |
| --- | --- | --- | --- |
|  |  |  | Blinks to indicate that the switch is actively sending or receiving data over that port. |
| 2 | 10/100 LNK/ ACT | Green | To indicate the link through that port is successfully established with speed 10Mbps or 100Mbps |
|  |  |  | To indicate that the switch is actively sending or receiving data over that port. |

C. PoE LED (IFS GE-DS-82-PoE)

| 1. | PoE In-Use | Amber | Illuminates to indicate the port is providing 48VDC in-line power. |
| --- | --- | --- | --- |
|  |  |  | Off to indicate the connected device is not a PoE Powered Device (PD). |

2.07 CONNECTORS

- Optical: SFP slot

- Power:  Universal AC socket

- Data: RJ-45

- Console: DB9 Type RS-232 serial com.

2.08 ELECTRICAL SPECIFICATIONS

- Power Characteristics of the IFS GE-DS-82:

- Voltage Input:100~240V AC / 50-60Hz

- Current: 0.2A max.

- Power Consumption: Maximum 12.2Watts

- Power Characteristics of the IFS GE-DS-82-PoE:

- Voltage Input:100~240V AC / 50-60Hz

- Current: 1.5A max.

- Power Consumption: Maximum 135Watts with PoE full load

- PoE Output Power of the IFS GE-FS-82-PoE:

- PoE output budget: 180Watts

- IEEE 802.3af class 3 (15.4W): Max. 8 ports

2.09 MECHANICAL SPECIFICATIONS

- Surface Mount Dimensions: 13” x 6.10” x 1.71” / 330 x 155 x 43.5mm, 1U height

- Finish: Module shall be constructed of a metal enclosure with a powder coat.

- Weight: <3.49 lbs./1.58kg

2.10 ENVIRONMENTAL SPECIFICATIONS

- MTBF: > 50,000 Hours

- Operating Temp: 0˚ C to +50˚ C

- Storage Temp: -20˚ C to +70˚ C

- Relative Humidity: 20% to 95% (non-condensing).

2.11 REGULATORY AGENCIES/APPROVALS AND LISTINGS

- Underwriters Laboratory (UL) Listing Number: I.T.E. 6D16

- Underwriters Laboratory Canada (ULC) Listing Number: I.T.E. 6D16

- Federal Communications Commission (FCC) Part 15, Class A

- European Union Compliance (CE) with following standard:

- EN 55022:2006, Class A

- EN61000-3-2:2006

- EN61000-3-3+A2:2005

- EN 55024+A2:2003

2.12 ACCESSORIES

- AC Power cord

- Rubber feet

- Rack-mount brackets

- RS-232 DB9 male console cable

PART 3 - EXECUTION

3.01 PREPARATION

- Standalone Module (Surface Mount)

- Shall be mounted on a properly prepared surface adequate for the size and weight of module.

- The placement of the unit shall allow provision for cable installation and maintenance as indicated on the approved detail drawings and in compliance with the installation manual.

- Rack Mount Module (19” Rack)

- The unit is installed in a standard EIA 19” (482.6 mm) rack or wall standoff bracket adequate for the size and weight of the rack mount unit. The placement of the unit shall allow provision for cable installation and maintenance as indicated on the approved detail drawings and in compliance with the user’s manual.

- Optical Fibers

- Caution: NEVER look into the end of an active optical fiber when using laser light output. Eye damage can occur. Wear eye protection when cleaving, terminating, and splicing fiber.

- The number of optical fiber SFP slot shall meet the requirements of the IFS model number.

- All optical fiber cables shall be properly installed and terminated with the mating optical connectors.

- The optical link shall be tested with either a power meter, at a minimum, or OTDR to ensure the link budget (overall path loss) plus an added 3dB of optical safety margin does not exceed the optical power budge.

3.02 INSTALLATION

- General: Locate fiber optic modules as indicated on the approved detail drawings and install module in compliance with the IFS User’s manual.

3.03 TESTING

- Testing the Fiber Optic Ethernet Link.

- Verify that the data leads and optical fibers are properly connected.

- Make sure that power is applied to all fiber optic modules, controllers, and receiver drivers or other equipment used in the system.

- Successful data link operation should be confirmed at this point by communicating with other equipment.

- Testing the 10/100TX Fast Ethernet Copper Link.

- Verify that the data leads and UTP ports are properly connected.

- Make sure that power is applied to the PoE switch.

- Successful data link operation should be confirmed at this point by communicating with other equipment.

- Testing the 10/100TX PoE Copper output capability.

3.04 CLEANING

- Follow all instructions for proper use of solvents and adhesives used for termination and splicing.

- At completion of the installation, dispose of all fiber scraps properly.

# MANUFACTURED UNITS REFERENCE TABLES

Table A: Product Number Descriptions

| IFS PART NO. | DESCRIPTION | MAX. DISTANCE* |
| --- | --- | --- |
| GE-DS-82 | 8-Port 10/100Base-TX + 2- Gigabit TP/SFP Managed Switch | Varies with SFP module |
| GE-DS-82-PoE | 8-Port 10/100Base-TX + 2- Gigabit TP/SFP Managed PoE Switch | Varies with SFP module |

* Maximum distance is limited to optical loss of the fiber and any additional loss by connectors, splices and patch panels.

Table B: Product Compatibility Chart

| IFS Ethernet Switch | COMPATIBLE EQUIPMENT |
| --- | --- |
| GE-DS-82 GE-DS-82-PoE | IEEE 802.3u standard TX and FX base for 10/100TX and 100FX protocol IEEE 802.3ab standard copper base for 1000Base-T protocol IEEE 802.3z standard fiber base for 1000Base-SX/LX IEEE 802.3af Power over Ethernet |

## END OF SECTION