### TruVision Integrated 36X PTZ Camera

- General

  - The TruVision PTZ Dome Camera shall be a dome camera system consisting of camera, pan/tilt driver unit, housing, and bubble.

  - The camera module, housing, and pan/tilt driver unit shall be as manufactured by Interlogix or an approved equal.

- Product

  - The camera system shall consist of a dome drive with a variable speed/high speed pan/tilt drive unit with continuous 360( rotation; 1/4-inch high resolution color/black-white CCD camera; motorized zoom lens with optical and digital zoom; auto focus.

  - The camera system shall meet or exceed the following design and performance specifications:

    - Generic characters:

      - The camera system shall offer a 36x 1/4-in. Sony Super HAD II CCD camera with 12x digital zoom.

      - The camera signal system shall be available in NTSC or PAL video signal format.

      - The camera system scanning shall be 2:1 interlacing.

      - The camera system shall be true day/night with a removable IR cut filter.

      - The camera system shall offer a selectable wide dynamic range (WDR) function.

      - The camera system shall offer a backlight compensation function.

      - The camera system shall have automatic white balance and also be capable of manual setup for white balance via the menu system.

      - The camera system shall have automatic iris control and manual override.

      - The camera system shall offer backlight compensation while in automatic iris control mode.

      - The camera system shall offer selectable electronic image stabilization (EIS) function.

      - The camera system shall offer motion detection function. When a motion is detected at the defined zone, the camera system will trigger an alarm and/or move the camera to a preset point.

      - The camera system shall allow privacy masks to conceal sensitive areas (such as neighboring windows) to protect them from view.

      - The camera system shall support the following tour modes:

        - Preset point: Max. 256 preset positions can be recalled.

        - Auto-pan: pan continuously between right and left limit settings.

        - Sequence: executes pre-positioning of the pan, tilt, zoom, and focus features in a certain sequence.

        - Cruise: a route formed with manual operation, through adjusting pan and tilt position, which can be stored and recalled to execute repeatedly.

      - The camera system shall offer auto- calibration function to check the camera’s position change during installation or maintenance and reset the camera to original position.

      - The camera system shall offer proportional speed function to decreases the pan/tilt speed when the camera is zoomed in.

      - The camera system shall offer a pan range of 360 degrees of endless rotation.

      - The camera system shall offer a tilt range of -10 to 190 degrees with digital image flip function.

      - The camera system shall offer pan and tilt preset repeatability accurate to within ±0.225 degrees.

      - The camera system shall offer the following variable pan/tilt speeds

        - Manual speed: 0.5 to 90 degrees per second.

        - Preset speed: 5 to 400 degrees per second

      - The camera system shall offer 16 independent titles with Max. 20 characters.

      - The camera system shall be able to be mounted to a wall, mounted to a surface, mounted to a pipe, or recessed into an indoor ceiling.

      - The camera system shall offer IP66 environmental protection for outdoor models and IP54 protection for indoor models.

      - The camera system dome bubble shall:

        - Meet flame, crush, and impact resistant requirements able to exceed UL 746C standard for polymeric material enclosures.

        - offer a high-resolution bubble made of acrylic and smoked bubble as option

    - Camera specification:

      - The camera system shall offer the following optical specification:

        - Total pixels: 1028X508, NTSC; 1028X596, PAL

        - Effective pixels: 480K, NTSC; 570K, PAL

        - Horizontal resolution: 650 TVL

        - Video output: 1.0 Vp-p, 75 ohms

        - Zoom: Optical 36x, digital 12x

        - Lens: F=3.4 mm (wide) to 122.4 mm (tele); F1.6 to F4.5

        - Scanning system: NTSC/PAL

        - Synchronization: Internal and line lock

        - Sensitivity: 0.1 lux at color mode; 0.01 lux at black/white mode

        - Electronic shutter speed: 1/1 to 1/10,000 sec, NTSC; 1/1 to 1/10,000 sec, PAL

        - Video Signal-to-Noise: >50dB( AGC off)

    - Housings, mounting and accessories:

      - Housings specifications

        - Outdoor housing:

          - Power Source: AC 24V ± 10%

          - Operating Temperature : -40 °C ~ 50 °C (-40 °F ~ 122 °F)

          - Dimension: Ø 191.97 × 282.11 mm (Ø 7.55 × 11.1 inches.) w/ Sunshield

          - Weight: 2.32 Kg (5.11 lbs)

          - IP 66 weather-proof

        - Indoor housing:

          - Power Source: AC 24V ± 10%

          - Operating Temperature : 0 °C ~ 40 °C (32 °F ~ 104 °F)

          - Dimension: Ø 171.7 × 228.7 mm (Ø 6.76 × 9 inches)

          - Weight: 1.62 Kg (3.57 lbs)

        - Connections.

          - Coaxial video: BNC

          - Control: Removable terminal strip

          - Power input: Two-position removable terminal strip

        - Each housing shall have site-tied memory so that camera is power-off or switched between housings, the settings shall remain the same.

      - Mounting options:

        - Surface-mount

          - The indoor camera model shall support surface mounting as a default. A hard ceiling mount bracket shall be shipped with the indoor camera.

        - Flush-mount

          - A flush mount (in-ceiling mount) shall be usable to suspend indoor dome.

        - Wall-mount

          - The outdoor camera model shall support wall mounting directly and do not require an adapter to attach wall mount bracket.

          - An indoor wall mount adapter shall be usable with wall mount bracket to suspend indoor dome.

        - Pendant-mount

          - A 1.5” NPT male adapter shall be usable with user supplied pipe to suspend an outdoor dome.

          - An indoor wall mount adapter mount and a 1.5” NPT pendant adapter shall be usable with user supplied pipe to suspend an indoor dome.

      - Bubble options:

        - Clear acrylic (no light loss)

        - Smoke acrylic (approximately 1/2 f-stop light loss)

      - Optional mounting accessories.

        - Flush-mount kit

          - The flush-mount kit shall include one ceiling mount, flush mount ring, trim ring and installation sticker

          - The ceiling mount and ring shall distribute the weight of the dome to the ceiling for greater stability.

          - The kit shall require a minimum load of 50 pounds when used with the flush-mount housing.

          - The kit shall have the following additional specifications:

            - Weight: 2.4lbs (1.1kg)

            - Construction: Steel

            - Finish: Galvanized

        - Wall-mount bracket

          - The cast-aluminum wall-mount arm shall be used to mount a dome to a vertical surface.

          - The wall-mount arm shall be for indoor or outdoor use.

          - The wall-mount arm shall be capable of being attached directly to a vertical surface or mated with a corner-mount, pole-mount, or roof-mount bracket.

          - The wall-mount arm shall have the following additional specifications:

            - Weight: 4.0 lb. (1.8 kg)

            - Construction: Aluminum

            - Finish: Gray

      - Corner-mount adapter

        - The corner-mount adapter shall be used to mount a dome to the corner of a building.

        - The corner-mount adapter shall be usable with a wall-mount arm to suspend the dome.

        - The adapter shall also be able to mount a power supply.

        - The adapter shall require a minimum load of 50 pounds when used with all housings.

        - The adapter shall have the following additional specifications:

          - Weight: 1.9 lb. (0.86 kg)

          - Construction: Aluminum

          - Finish: Gray powder coat

      - Pole-mount adapter

        - The pole-mount adapter shall be used to mount a dome to a pole.

        - The pole-mount adapter can be attached to the pole using bolts or three adjustable stainless-steel bands, not included with the adapter.

        - The adapter shall be usable with a wall-mount arm or gooseneck wall-mount arm to suspend the dome.

        - The adapter can also be used to mount a power supply.

        - The adapter shall require a minimum load of 50 pounds when used with all housings.

        - The adapter shall have the following additional specifications:

          - Weight: 14.4 oz. (408 g)

          - Construction: Aluminum

          - Finish: Gray powder coat

    - Communication:

      - The camera system shall offer DIP switches for setting the camera’s site address and control protocol.

      - The camera system shall be compatible with the following protocols for data transmission and control:

        - INTERLOGIX Digiplex RS422

        - INTERLOGIX Impac RS485

        - Pelco D

        - Pelco P

        - Philips

        - AD422

        - JVC

        - Panasonic

        - VCL

        - DSCP

        - DMP

        - Chiper

    - Menu

      - The camera system shall use a menu-based system for programming the camera and pan/tilt unit.

      - A compatible keypad or other control device can be used to navigate through the menus.

      - The menus shall have the following options:

        - Language selections: configures the language of the on-screen display

          - The supported languages shall include English, French, German, Italian, Portuguese, and Spanish.

          - The default language is English

        - Default camera: configures the remote system reset, or is used to default all the settings of the system or of a dome camera.

        - Backlight: enable/disable the backlight setting.

        - Focus: configures focus to be manual or auto.

        - AE mode: configures exposure compensation, shutter speed, and iris control.

        - WBC mode: configures white balance.

        - SETUP MENU 1: configures digital zoom, automatic slow shutter, digital noise reduction, video invert, image freeze, aperture, and stabilizer.

        - SETUP MENU 2: configures image flip, tilt limits, proportional speed, auto calibration, password, OSD menu duration, system reset.

        - ID display: configures the camera site ID.

        - Title display: configures the camera title display.

        - Title setting: configures the wording of the camera title.

        - Preset: configures preset points.

        - Sequence: configures sequence, sequence step, preset position, sequence speed, dwell time, and manual sequence.

        - Auto-pan: configures auto-pan, start point, end point, direction, speed, and execution.

        - Cruise: configures the cruise number, record start, and record end.

        - Home setting: configures home, return action selection, preset point selection, sequence selection, auto-pan selection, cruise selection, return time, and manual home.

        - IR function: configures IR cut filter threshold, and manual control.

        - Alarm setting: configures alarm settings.

        - Alarm detect: configures alarm detection.

        - WDR function: enable/disable the wide dynamic range feature.

        - Privacy mask: configures the privacy mask.

        - Time setting: configures the time and date of the dome camera.

        - Schedule: configures schedules for presets/sequence/auto-pans/cruises/IR function.

    - Recognized compliance standards:

      - FCC

      - CE

      - C-Tick

      - RoHS