DIVISION 27 21 29

IFS 8 PORT GIGABIT SWITCH WITH 4 POE PORTS

ES3002-4P-4T

ENGINEERING SPECIFICATIONS

# PART 1 - GENERAL

1.01 SUMMARY

- Eight 10/100/1000Base-T Copper  Port with Four PoE-AT Gigabit Unmanaged Switch

1.02 SECTION INCLUDES

- IFS ES3002-4P-4T 8-Port Gigabit Switch with 4 PoE Ports– Standalone

1.03 REFERENCES

- Federal Communications Commission (FCC)

- European Union Compliance (CE)

1.04 SYSTEM DESCRIPTION

- Performance Requirements: Provide 8 10/100/1000Base-T copper ports with 4 IEEE 802.3at Power over Ethernet Injector.

- The system shall utilize EIA568, category 5/5e/6, 4-pair cables for 10Base-T or 100Base-TX and 1000Base-T to transfer Ethernet data and 53V DC power simultaneously.

1.05 SUBMITTALS

- Manufacturer’s Installation and Operating Manual: Printed installation and operating information for the unmanaged PoE Switch.

- Warranty: Manufacturer’s Printed Warranty.

1.06 DELIVERY, STORAGE AND HANDLING

- Store in original packaging in a climate controlled environment.

- Storage Temperature not to exceed: -10˚ C to +70˚ C

1.07 PROJECT/SITE CONDITIONS

- Temperature Requirements: Products shall operate in an environment with an ambient temperature range of 0˚ C to +50˚ C without the assistance of fan-forced cooling.

- Humidity Requirements: Products shall operate in an environment with relative humidity of 5% to 95% (non-condensing).

1.08 WARRANTY

- Standard UTC Fire & Security Inc. Comprehensive Warranty: UTC Fire & Security warrants the product to be free of factory defects under manufacture’s 3 Years Warranty.

# PART 2 - PRODUCTS

2.01 MANUFACTURER

- Acceptable Manufacturer:

- IFS Brand

UTC Fire & Security, Inc.

3211 Progress Drive

Lincolnton, NC 28092

- Phone 1-855-286-8889

- Email: presales@interlogix.com

- Substitutions: Not Permitted

2.02 MANUFACTURED UNITS

- Model Number Descriptions: Reference Table A: Product Number Descriptions

2.03 GENERAL SPECIFICATIONS

- The Gigabit PoE Unmanaged Switch shall be an ES3002-4P-4T model.

- The Gigabit PoE Unmanaged Switch with 8 10/100/1000Base-T copper ports.

- The 10/100/1000Base-T port shall support the Ethernet data IEEE 802.3 protocol using Auto-negotiating and Auto-MDI/MDI-X features.

- The switch shall be connected with EIA568A/B Cat 5/5e/6 UTP/STP cable system for its RJ45 interface ports.

- The ES3002-4P-4T shall comply with IEEE 802.3at Power over Ethernet:

- The ES3002-4P-4T shall support IEEE 802.3at Power over Ethernet detection and 53VDC power injection at port1 to port4.

- The ES3002-4P-4T is also the power injectors which transmit DC Voltage to the Cat5/5e/6 cable and transfer data and power simultaneously to remote PD (Powered Device) equipments.

- The ES3002-4P-4T shall Auto-detect of PoE IEEE 802.3at equipment; protect devices from being damaged by incorrect installation.

- The ES3002-4P-4T shall support total distance up to 100 meters on PoE ports.

2.04 DATA SPECIFICATIONS

- Data Interface: Ethernet IEEE802.3/3u/3ab

- Data Rate:

- Port 1 to Port 8: 10/100/1000 Mbps

- Data Inputs: 8

- Ports 1 to 4 switch selectable to operate at

either 100m in standard mode or 200m in

10 MHz mode.

- Operation Mode: Simplex or Duplex

2.05 STATUS INDICATORS

- System

| 1. | PWR | Green | Lit: indicates that this device has been powered. |
| --- | --- | --- | --- |
|  | PoE max. | Green | Lit: indicates PoE budget usage is full. |

B. 10/100/1000Base-T Interfaces

| 1. | 10/100/1000 LNK/ACT | Green | Lit: indicates that the port is successfully connecting to the network at 1000 Mbps. |
| --- | --- | --- | --- |
|  |  |  | Blink: indicates that the switch is actively sending or receiving data over that port. |
|  |  | Amber | Lit: indicates that the port is successfully connecting to the network at 10/100 Mbps. |
|  |  |  | Blink: indicates that the switch is actively sending or receiving data over that port. |
| 2. | PoE In-use | Orange | Lit: indicates the port is providing 53V DC in-line power. (1-4 ports only) |

2.06 CONNECTORS

- Power:  Universal AC socket

- Data: RJ45

2.07 ENVIRONMENTAL SPECIFICATIONS

- MTBF: > 50,000 Hours

- Operating Temp: 0˚ C to +50˚ C

- Storage Temp: -10˚ C to +70˚ C

- Relative Humidity: 5% to 95% (non-condensing).

2.08 REGULATORY AGENCIES/APPROVALS AND LISTINGS

- Federal Communications Commission (FCC) Part 15, Class A

- European Union Compliance (CE)

2.09 ACCESSORIES

- AC Power cord

- Rubber feet

- Rack-mount ear kit

PART 3 - EXECUTION

3.01 PREPARATION

- Standalone Module (Surface Mount)

- Shall be mounted on a properly prepared surface adequate for the size and weight of module. The placement of the unit shall allow provision for cable installation and maintenance as indicated on the approved detail drawings and in compliance with the installation manual.

3.02 INSTALLATION

- General: Locate fiber optic modules as indicated on the approved detail drawings and install module in compliance with the UTC Fire & Security User’s manual.

3.03 Cleaning

- Follow all instructions for proper use of solvents and adhesives used for termination and splicing.

3.04 TESTING

- Testing the 10/100/1000Base-T Gigabit Ethernet and Gigabit Copper Link.

- Verify that the data leads and UTP ports are properly connected.

- Successful data link operation should be confirmed at this point by communicating with other equipment.

- Testing the 10/100/1000Base-T PoE Copper output capability.

# MANUFACTURED UNITS REFERENCE TABLES

Table A: Product Number Descriptions

| IFS PART NO. | DESCRIPTION | MAX. DISTANCE* |
| --- | --- | --- |
| ES3002-4P-4T | 8 PORT GIGABIT SWITCH WITH 4 POE PORTS | 300 feet (100M) electrical |

## END OF SECTION